C256jr User Manual
# Introduction
# Memory Layout and Management
The JUNIOR can support up to 1MB of memory, divided into RAM and flash. The overall memory map looks like:
$00000	System RAM
$3FFFF
$40000	Reserved for future expansion
$7FFFF
$80000	Flash memory (512KB)
$FFFFF

The JUNIOR uses the Western Design Center’s 65C02 processor for its CPU, which is limited to only 64K of address space. So, how can it access all that memory that’s on the board? One of the features in the JUNIOR is a memory management unit, or MMU. This MMU allows the CPU to switch different sections of the system memory into and out of the CPU’s address space.
Memory on the JUNIOR is divided up into 8KB blocks or banks of memory. From the CPU’s perspective, there are eight of them:
Bank	Start	End
0*	$0000	$3FFF
1	$2000	$3FFF
2	$4000	$5FFF
3	$6000	$7FFF
4	$8000	$9FFF
5	$A000	$BFFF
6*	$C000	$DFFF
7	$E000	$FFFF

Similarly, RAM and Flash are divided up into 8KB banks, starting at $00000 and ending at $FFFFF. The MMU can map any of the eight CPU banks to any of the banks of RAM or Flash. It does this through memory access lookup tables (LUT).
Each LUT translates an access in the CPU address space to the corresponding location in the system’s full address space. The translation is very straightforward. Each LUT has eight 7-bit entries, one for each of the eight banks of CPU address space. The lower 13 bits of the CPU address are taken for the lower 13 bits of the full system address. The upper three bits select an entry in the LUT, and the seven bits in the entry provide the upper 7 bits of the system address.
The MMU supports four lookup tables. One table is selected as the active translation table at any given time, and the CPU can switch the active table whenever necessary. It is also possible for the CPU to edit any of the tables (whether or not it is the active LUT). In this way, the CPU can access any part of memory but can very quickly switch between as many as four separate memory layouts.
Most of the banks are simply mapped to a bank in either RAM or Flash, but two are special: bank 0, and bank 6. While both banks can be mapped to memory like the others, they can also serve special I/O functions.
Bank 6, in addition to being mapped to RAM or flash can also be mapped to one of four I/O “pages”. I/O pages 0 and 1 are where most of the I/O and control registers of the JUNIOR are located. I/O page 2 is where the text matrix is located, and I/O page 3 is where the color matrix for text is located.
Bank 0 provides access to memory, but it also provides access to the MMU control registers. Finally, there is an option for bank 0 to also provide access to either the text or the color matrices for the text display.
## MMU Operation
There are two master control registers for the MMU. These two registers are always present in bank 0, regardless of the settings.
Address	7	6	5	4	3	2	1	0
$0000	LUT_ACC_EN	X	EDIT_LUT		X	X	ACT_LUT
$0001	X	X	X	X	X	DSBL_IO	ACT_IO_PAGE

These registers allow you to do three main things:
- Select one of the four LUTs as the active LUT to use for address translation
- Edit one of the LUTs to change how the CPU address banks map to system address banks.
- Map CPU bank 6 to either I/O registers (including the text and color matrices for the text screen) or memory
To select a LUT to be the current address translation table, you set ACT_LUT to the number of the LUT: 00 for LUT#0, 01 for LUT#1, 10 for LUT#2, and 11 for LUT#3.
To select a bank of I/O registers to be visible in bank 6, set DSBL_IO to 0 and ACT_IO_PAGE to the number of the I/O page you want. To have memory be present at bank 6, set DSBL_IO to 1, then bank 6 will be mapped to memory using the LUT.
I/O Page	Purpose
0	The majority of the I/O registers will be here (sound devices, serial ports, the graphics system).
1	The data for the text mode font is here, along with the color lookup tables for the various graphics modes.
2	The text matrix for the text screen. This is the actual character data shown on the screen.
3	The color matrix for the text screen. You can control the foreground and background colors of the individual characters here.

To edit a LUT, you set the bits EDIT_LUT to the number of the LUT you want and set LUT_ACC_EN to 1. Then the entries for the LUT go in addresses $0008 through $000F:
Bank	Address	7	6	5	4	3	2	1	0
0	$0008	X	SA19	SA18	SA17	SA16	SA15	SA14	SA13
1	$0009	X	SA19	SA18	SA17	SA16	SA15	SA14	SA13
2	$000A	X	SA19	SA18	SA17	SA16	SA15	SA14	SA13
3	$000B	X	SA19	SA18	SA17	SA16	SA15	SA14	SA13
4	$000C	X	SA19	SA18	SA17	SA16	SA15	SA14	SA13
5	$000D	X	SA19	SA18	SA17	SA16	SA15	SA14	SA13
6	$000E	X	SA19	SA18	SA17	SA16	SA15	SA14	SA13
7	$000F	X	SA19	SA18	SA17	SA16	SA15	SA14	SA13

If LUT_ACC_EN is 0, addresses $0008 through $000F will be ordinary memory locations. The LUT is only present there if LUC_ACC_EN is 1.
### Example: Setting Up an Address Lookup Table
In this example, we want to initialize the CPU memory map so that all banks go to RAM except for bank 6, which should go to I/O page 1 and bank 7, which should go to the first bank of flash memory. The LUT should look like this:
CPU Bank	System Bank
$00	$00
$01	$01
$02	$02
$03	$03
$04	$04
$05	$05
$06	I/O Page 0
$07	$80

First, we need to enable editing of a LUT and select LUT #0 to be edited:
lda #$80	; Edit enabled, LUT#0 selected for edit
sta $0001
Now, addresses $0008 through $000F should be going to LUT #0, and we can write our mappings:
ldx #0	; Start at bank 0
l1:	txa	; The CPU bank and System bank will be the same
sta $0008,x	; Set the System bank to use for this bank
inx	; Move to the next bank
cpx #7	; Until we reach bank #7
bne l1

lda #$40	; CPU Bank 7 will map to System Bank $40
sta $000f	; Set bank 7

stz $0000	; Select LUT#0 as active, turn off editing

Now, we need to map bank #6 to the I/O page #0:
stz $0001	; Set DSBL_IO to 0 and set I/O Page to 0
One thing to notice with this example is that the entry in the LUT for bank #6 is 6. This is just for completeness. That mapping is ignored since we are mapping the I/O page to bank #6. If at some point in the program, DSBL_IO is set to 1, then system RAM bank 6 would appear there.

# Displays
The display on the JUNIOR is managed by TinyVicky, which is the smaller member of the Vicky family of display controllers in the other Foenix machines. TinyVicky provides several display engines to let your programs control the screen:
- Text: an old school style text screen where the characters to display are stored in a text matrix, and the shape of those characters comes from font memory. Text mode characters are 8 pixels wide by 8 pixels high.
- Bitmap: a simple pixel graphics mode that can be either 300x240 or 300x200. TinyVicky supports two layers of bitmap
- Sprite: an engine to display small, movable sprites on the screen. [TODO: how many and what resolutions]
- Tile: an engine to display images on the screen made up of tiles from a tile set [TODO: how many layers, tile size]
The bitmap, sprite, and tile engines are considered graphics modes. TinyVicky will let you display either text by itself, a mix of the graphics modes by themselves, or text overlayed on top of the graphics modes.
[TODO: resolutions?]
## Text Display
#### Text Matrix
The memory for the characters to display on the screen is the text matrix, which is stored in I/O page #2. When this I/O page is swapped into the CPU address space, it appears at $C000. Each byte of memory corresponds to a single character on the screen in left to right, top to bottom order. The byte at $C000 is the upper left corner of the screen, the byte at $C001 is the next character to the right, and so on. The number of bytes per line is set by the base resolution of the screen, but is generally 80. When a border is displayed, while that limits the number of characters displayed, the layout in memory remains the same.
##### Example: Print an A to the Screen
lda $0001	; Save the current MMU setting
pha

lda #$02	; Swap I/O Page 2 into bank 6
sta $0001

lda #’A’	; Write ‘A’ to the upper left corner
sta $C000

pla	; Restore the old MMU setting
sta $0001

Note: this example does not set the font or the color, so depending on how your JUNIOR is initialized, you may not see an actual “A” on the screen.
#### Text Color LUTs
Characters in TinyVicky text mode have two colors: the foreground and the background. The foreground and background colors are picked for each character out of two different palettes of 16 colors each. The colors in the palettes are picked from the full range of colors JUNIOR can produce, which is more than 16 million colors. This is all managed through two color lookup tables (LUTs) provided by TinyVicky: a text foreground color LUT, and a text background color LUT.
The text LUTs are stored in I/O page #0. The foreground LUT starts at $D800, and the background LUT starts at $D840.
Each LUT is a list of 16 entries. Each entry is a set of four bytes: blue, green, red, and alpha. Each byte indicates how much of that primary color is present as a component of the actual color. The values range from 0 (none) to 255 (as much as possible). Currently, the alpha channel is not used and is there for future expansion.
#### Color Matrix
The way that text color is selected for each character is through the color matrix. This section of memory is in I/O page #3 and starts at $C000 when page #3 is swapped into the CPU’s address space. The layout is precisely the same as the text matrix (e.g. the character at $C123 in the text matrix has its color information at $C123 in the color matrix).
Each byte in the color matrix specifies two colors by providing an index into each of the two text LUTs. The most significant four bits is the number of the foreground color to use. The number of the least significant four bits is the number of the background color to use.
Let’s say the color value at $C123 is $45. This means that the foreground color of the character is color #4 from the text foreground LUT, which starts at $D810 ($D800 + 4 * 4), and the background color of the character is #5 from the text background LUT, which starts at $D854 ($D840 + 4 * 5). If the bytes at $D810 are $00, $80, $80, that means the foreground will be a medium yellow. If the bytes at $D854 are $FF, $00, $00, that means the background will be blue.
##### Example: Make That “A” Yellow on Blue
lda $0001	; Save the MMU state
pha

stz $0001	; Switch in I/O Page #0

stz $D810	; Set foreground #4 to medium yellow
lda #$80
sta $D811
sta $D812

lda #$FF	; Set background #5 to blue
sta $D854
stz $D855
stz $D856

lda #$03	; Switch to I/O page #3 (color matrix)
sta $0001

lda #$45	; Color will be foreground=4, background=5
sta $C000

pla	; Restore the MMU state
sta $0001

## Bitmap Displays
## Sprites
## Tiles
# Sound
## Programmable Sound Generator (SN76489)
## SID
## CODEC
# Interrupt Controller
# Time
## Timers
## Real Time Clock
# Math Coprocessor
# SD Card
# Serial Communication
## IEC Serial Port
## RS-232 Serial Port
# Input Devices
## Joysticks
## PS/2 Keyboard and Mouse
Appendix
# Programming in C
# The Debug Port