C256jr User Manual
# Introduction
# Memory Layout and Management
The JUNIOR can support up to 1MB of memory, divided into RAM and flash. The overall memory map looks like:
$00000	System RAM
$3FFFF
$40000	Reserved for future expansion
$7FFFF
$80000	Flash memory (512KB)
$FFFFF

The JUNIOR uses the Western Design Center’s 65C02 processor for its CPU, which is limited to only 64K of address space. So, how can it access all that memory that’s on the board? One of the features in the JUNIOR is a memory management unit, or MMU. This MMU allows the CPU to switch different sections of the system memory into and out of the CPU’s address space.
Memory on the JUNIOR is divided up into 8KB blocks or banks of memory. From the CPU’s perspective, there are eight of them:
Bank	Start	End
0*	$0000	$3FFF
1	$2000	$3FFF
2	$4000	$5FFF
3	$6000	$7FFF
4	$8000	$9FFF
5	$A000	$BFFF
6*	$C000	$DFFF
7	$E000	$FFFF

Similarly, RAM and Flash are divided up into 8KB banks, starting at $00000 and ending at $FFFFF. The MMU can map any of the eight CPU banks to any of the banks of RAM or Flash. It does this through memory access lookup tables (LUT).
Each LUT translates an access in the CPU address space to the corresponding location in the system’s full address space. The translation is very straightforward. Each LUT has eight 7-bit entries, one for each of the eight banks of CPU address space. The lower 13 bits of the CPU address are taken for the lower 13 bits of the full system address. The upper three bits select an entry in the LUT, and the seven bits in the entry provide the upper 7 bits of the system address.
The MMU supports four lookup tables. One table is selected as the active translation table at any given time, and the CPU can switch the active table whenever necessary. It is also possible for the CPU to edit any of the tables (whether or not it is the active LUT). In this way, the CPU can access any part of memory but can very quickly switch between as many as four separate memory layouts.
Most of the banks are simply mapped to a bank in either RAM or Flash, but two are special: bank 0, and bank 6. While both banks can be mapped to memory like the others, they can also serve special I/O functions.
Bank 6, in addition to being mapped to RAM or flash can also be mapped to one of four I/O “pages”. I/O pages 0 and 1 are where most of the I/O and control registers of the JUNIOR are located. I/O page 2 is where the text matrix is located, and I/O page 3 is where the color matrix for text is located.
Bank 0 provides access to memory, but it also provides access to the MMU control registers. Finally, there is an option for bank 0 to also provide access to either the text or the color matrices for the text display.
## MMU Registers
There are two master control registers for the MMU. These two registers are always present in bank 0, regardless of the settings.
Address	7	6	5	4	3	2	1	0
$0000	LUT_ACC_EN		EDIT_LUT				ACT_LUT
$0001			TEXT_LOC	TEXT_COL		DSBL_IO	ACT_IO_PAGE

- ACT_LUT: This two bit value selects which LUT is the active one to use for address translations. 00 = LUT0, 01 = LUT1, 10 = LUT2, and 11 = LUT3.
- EDIT_LUT: This two bit value selects which LUT is available to be edited. This field only has meaning if LUT_ACC_EN is 1.
- LUT_ACC_EN: This single bit value selects whether or not LUTs can be accessed by the CPU for editing. If LUC_ACC_EN = 0, the LUT registers are not accessible. If LUC_ACC_EN = 1, the LUT registers are accessible, and the LUT indicated by EDIT_LUT is the one exposed.
- ACT_IO_PAGE: This two bit value selects which page of I/O registers is available in bank 6 (00 = I/O 0, 01 = I/O 1, 10 = text matrix, 11 = color matrix).
- DSBL_IO: This one bit value selects if bank 6 is memory or I/O (0 = the I/O page selected by ACT_IO_PAGE is in bank 6, 1 = the memory indicated by the active LUT is in bank 6).
- TEXT_LOC: If this bit is 1, address from $0400 through $1FFF are mapped to either the text matrix or the color matrix. If this bit is 0, those addresses are mapped to the memory indicated by the active LUT.
- TEXT_COL: If TEXT_LOC is 1, this bit will select between the text matrix being at $0400 (0), or the color matrix (1).
# Displays
## Text Display
## Bitmap Displays
## Sprites
## Tiles
# Sound
## Programmable Sound Generator (SN76489)
## SID
## CODEC
# Interrupt Controller
# Time
## Timers
## Real Time Clock
# Math Coprocessor
# SD Card
# Serial Communication
## IEC Serial Port
## RS-232 Serial Port
# Input Devices
## Joysticks
## PS/2 Keyboard and Mouse
Appendix
# Programming in C
# The Debug Port